## Slide 1
Problem Statement
Based on a given pair of latitude and longitude by the user, align the camera axis of the satellite (X-axis of satellite body frame) towards the point on the Earth defined by the input latitude-longitude pair.
Expected output
The rotation sequence to point the camera towards a specific point on the Earth.
Assumptions
1. The initial orientation of the satellite in LEO is random.
Future scope / In process
Add logic for continuous attitude measurement and adjustments to account for perturbations.
Add logic to factor in data from attitude measurement sensors like star trackers and IMUs to determine the specific attitude of the satellite at any point in orbit.
Pacific Palisades
Pacific Palisades
A
B
Y
Z
e.g. Point the X-axis of the satellite towards the Pacific Palisades located in the state of California in the US. Co-ordinates for the target location are 34.0467° N, 118.5464° W (Latitude 34.0467; Longitude -118.5464)

## Slide 2: Earth Model with ECEF reference frame and a vector pointing towards the target
The purpose of this step is to determine the point in LEO where the origin of the satellite body-reference frame needs to be.
The vector is plotted by using the cartesian co-ordinates derived from the following parameters:
Length = radius of LEO; Azimuthal angle = Longitude; Elevation = Latitude (Python function on the right)

## Slide 3: Randomly oriented satellite body frame at the specific LEO point as origin
The purpose of this step is to visualize a randomly oriented satellite in LEO. SCB stands for Spacecraft Body.
The decision to choose a random orientation is made because we need the algorithm to work on the entire space of possible satellite orientations.
The option to apply specific rotations is commented out but can be used to test out user-specified rotation sequences.
View 1
View 2
Note: The ‘from_euler’ function is available in Python for directly applying a rotation sequence but not used since we are building the logic for Euler angle calculations from scratch.

## Slide 4: A copy of the ECEF reference frame at SCB origin in LEO
To determine the rotation sequence for the SCB reference frame, I followed the approach of first measuring its orientation with respect to the ECEF reference frame.
The purpose for this alignment is that when the SCB reference frame aligns with the ECEF reference frame, the problem is then reduced to aligning rotations to SCB that are a function of the latitude and longitude data available to us.

## Slide 5: Step 1: Rotate about Zecef axis by the azimuthal angle of Xscb
View 1
View 2
Here we rotate the SCB reference frame about Zecef by the azimuthal angle of the Xscb axis. This is the first step towards aligning SCB with ECEF.
The rotation angle (‘azim_rotation_of_Xscb’ in the code) depends on where the satellite is located in the available 8 spaces. This is handled by the if…elif loop in the code.
The original reference frame is denoted by ‘…’, and the rotated reference frame is denoted by solid line with labels ‘…_Zrot’. e.g. Here we rotated Xscb by ~146 degrees to get to Xscb_Zrot

## Slide 6: Step 2: Rotate about Yecef axis by the elevation angle of Xscb
View 1
View 2
Here we rotate the SCB reference frame about Yecef by the elevation angle of the Xscb axis. This is the second step towards aligning SCB with ECEF. The direction cosine matrix is defined by the ‘dcm_rotation_abt_Yscb’ variable.
The rotation angle (‘elev_rotation_of_Xscb’ in the code) is the elevation angle of Xscb. By rotating Xscb by this angle we are now placing it in the Xyecef plane. This with the 1st rotation aligns Xscb with Xecef.
The original reference frame is denoted by ‘…’, and the rotated reference frame is denoted by ‘-.-.-’ with labels ‘…_Yrot’. e.g. Here we rotated Xscb by ~74 degrees to get to Xscb_Yrot.
Note: this is a different example from the previous slide as code needs to be executed multiple times for screenshots, each run starts with a randomly oriented SCB. RefFrame_Zrot is not shown to avoid congestion.

## Slide 7: Step 3: Rotate about Xecef axis by the angle between Zscb_Yrot and Zecef
View 1
View 2
Finally, we rotate SCB about the Xecef axis and this completes the rotation sequence required to align the SCB reference frame with the ECEF reference frame.
The python code is set up to calculate ‘polar_Zscb_for_rotation_about_Xecef’, which is the angle of rotation between Zscb and Zecef. The angle of rotation is dependent upon Zscb_Yrot’s alignment in space and is handled with the ‘if…elif’ code snippet.
‘_Xrot’ is the SCB reference frame that has undergone 3 rotations from its initial random rotation and is now aligned with the ECEF reference frame.
Note: this is a different example from the previous slide as code needs to be executed multiple times for screenshots, each run starts with a randomly oriented SCB. RefFrame_Yrot is not shown to avoid congestion.

## Slide 8: Step A: Rotate the ‘_Xrot’ reference frame about Yecef axis by the Latitude
View 1
View 2
After aligning the satellite body frame with the ECEF reference frame, we implement 2 more rotations to align the instrument (the Xscb_rotA axis in our case) towards the target location on Earth.
This is done by using the latitude and longitude data.
Step A will be a rotation about the Yecef axis by the latitude (34.0467 degrees in the Pacific Palisades example).
Note: this is a different example from the previous slide as code needs to be executed multiple times for screenshots, each run starts with a randomly oriented SCB. RefFrame_Xrot is not shown to avoid congestion.

## Slide 9: Step B: Rotate the ‘_rotA’ reference frame about Zecef axis.
View 1
View 2
This final step in the entire rotation sequence aligns the camera axis towards the exact latitude and longitude point on the Earths surface.
This rotation is achieved by rotating the ‘_rotA’ reference frame about the Zecef axis by an angle ‘longitude + 180’. The extra 180 degrees ensure that the camera is pointed towards the Earth.
Note: this is a different example from the previous slide as code needs to be executed multiple times for screenshots, each run starts with a randomly oriented SCB. RefFrame_rotA is not shown to avoid congestion.

## Slide 10: Entire rotation sequence applied + summary of the Python code
Output of the algorithm
Step 1: azim_rotation_of_Xscb: 14.88 (rotate about Zecef)
Step 2: elev_rotation_of_Xscb: -62.36 (rotate about Yecef)
Step 3: polar_Zscb_for_rotation_about_Xecef: -100.31
(rotate about Xecef)
Step A: Xscb_R_rotation_angle_about_Yscb_R: 34.04
(rotate about Yecef)
Step B: Xscb_R_rotation_angle_about_Zscb_R: 61.45
(rotate about Zecef)
Input of the algorithm
Output of the algorithm
The Python code takes user defined latitude and longitude values as input and generate a rotation sequence to point the instrument (i.e. camera) axis of the satellite towards the location defined by the input latitude longitude values.

## Slide 11: Why are maneuvers performed
Maintaining Orbit and Altitude – to keep the satellite at a desired altitude and speed, ensuring consistent data collection.
Maintaining a consistent ground track – For polar-orbiting satellites like Landsat, these maneuvers keep the satellite’s ground track and timing of its equatorial crossings consistent over time.
Counteracting Orbital Perturbations - The gravitational forces of the Sun and Moon, along with factors like solar radiation pressure and the weak effects of Earth’s non-uniform gravity, can alter a satellite’s orbit, requiring adjustments to stay on course.
Drag make-up (DMU) or Delta-Velocity (Delta-V) maneuvers – To increase the satellites orbital velocity to raise its altitude, counteracting the effects of atmospheric drag that would otherwise lower the orbit time.
Inclination Adjustment (IAM) or Delta-Inclination (Delta-I) maneuvers – These burns are performed to adjust the angle of orbit relative to the Earth’s equator, which is necessary for maintaining a consistent ground track for land-observing satellites and for managing the change in inclination caused by gravitational forces from the Sun and Moon.
Station-Keeping maneuvers – These are small adjustments to the satellite's orbit and position to counteract gradual orbital perturbations caused by the gravitational pull of the Moon and the Sun.
Longitudinal Shift Maneuvers – These maneuvers change the satellite’s sub-satellite point on the Earth’s equator, often by adjusting the satellite’s orbital period to match the Earth’s rotation for geostationary or geosynchronous orbits.
Types of maneuvers

## Slide 12: Design of the ADCS algorithm
Performance of the algorithm – metrics for delta between actual results & expected results

## Slide 13: Autonomous capabilities for ADCS
Neural Networks for State Estimation
Reinforcement Learning for Guidance & Control